## Slide 1: EnDev Indonesia MHP Troubleshooting Poster
A0 size poster (33.11 in x 46.81 in)
Landscape orientation
Full colour
Glossy paper, durable and weather resistant

## Slide 2
MHP: ____________________________
Operator: __________ HP: ___________
Manager: __________ HP: ___________
Connected to: ______ household
Total head: ____ m
Average flow: ____ l/s
MHP measured capacity: ____ kW
Date commissioned: ____ /____ /____
Is the generator/turbine belt squealing?
Shut down MHP
Adjust belt tension or replace worn belt
Is trash rack clean and free of obstruction?
Is frequency (Hz) in MHP control panel correct?
Less than 48 Hz
Does adjusting the guide vane at the turbine to reduce water flow correct the frequency (Hz) and reduce noise?
Is the ELC indicator light green?
Are there any loose anchor bolts?
Tighten bolts
Are there new electrical appliances or devices installed?
Switch new devices OFF
No
Fully open turbine water inlet (guide vane)
Are lights now brighter?
No
Check for MCB at households and try reducing load
(generator capacity is exceeded!)
Use only priority devices
Install mini circuit breakers (MCB) at households
Is the water flow to the turbine steady, uninterrupted and regular?
Is there trash and sediment in the forebay or channel?
Is there obstruction or trash in the weir?
Check for blockages in penstock and turbine guide vane
Yes
Yes
Yes
No
No
Check Voltage (220 V) at all households connected on the same distribution branch
1. Check for broken cable and reconnect
2. Check for too many electricity connections
No
Yes
50 Hz
Is circuit breaker switch to households at power house ON?
Is generator and turbine operating well?
Turn circuit breaker switch ON
Circuit breaker switch switched OFF again?
No
Yes
1. Check for short circuited wiring
and
2. Check overload at customers and try reducing load
(generator capacity is exceeded!)
Yes
No
Unusual Noise?
No Electricity?
Overheating?
Are ELC component burnt or ELC box too hot when touched?
Is ELC ventilation fan working well?
Clean fan and housing and replace fan if necessary
Are ballast fuse in ELC or ballast elements burnt or disconnected?
1. Check for water flow blockage
and
2. Check for overload at households , try reducing load
(generator capacity is exceeded!)
Is generator too hot when touched?
Is ventilation fan in generator housing blocked or dirty?
Is the load current (amp) on the ELC amp meter above normal?
Replace burnt elements, reconnect wires and/or replace fuse
Grease bearings and check for bearing defect
Is there a burnt smell from inside generator?
Stop MHP, open generator housing, check if cable winding is dirty?
Are there burn marks on the winding (short circuit!)?
Clean generator winding
Clean ventilation fan and housing
Reduce load by switching off appliances and/or users
(generator capacity is exceeded!)
Is the belt slipping when MHP is on?
Replace bearing
Adjust grease to normal use
Adjust belt tension
Yes
Yes
No
No
Yes
No
Yes
Yes
No
Yes
No
Yes
No
Defective bearing
Too much/
too little grease
Normal
Yes
Is problem solved after checking and fixing electricity in affected house?
TROUBLESHOOTING GUIDE FOR MICROHYDRO PROBLEMS
Yes
Yes
Yes
Yes
Civil Work Check
Civil Work Check
?
No Bright Light?
All customers
Some customers
One customer
Ask for Help
Technician name: ___________________________________________
Technician number: _________________________________________
Yes
No
Less than 220 V
Ask for Help
Technician name: ___________________________________________
Technician number: _________________________________________
220 V
Check for broken cable and reconnect
More than
52 Hz
Yes
No*
Clean trash rack
No
Yes
Clean forebay and channel
No
No*
No*
Check for blockages and obstructions in the river
No*
No
No
Ask for Help
Technician name: ___________________________________________
Technician number: _________________________________________
No*
1. Check for water flow blockages and
2. Check for water losses
No*
*two actions are possible, try each one until solved
MCB already installed at each customer
No MCB in customers yet
For unusual noises, check frequency in panel box
See frequency meter in control box
See if frequency is
  Too low: less than 48 Hz
  Normal : 48 – 52 Hz
  Too high: more than 52 Hz
If too low, then
  Check if there are any additional load/appliances
  Check for electricity stealing
  Check if flow into turbine is normal
If too high, then adjust water flow to turbine
If normal then check whether flow is unsteady or belt is squealing
etr
48 Hz
52 Hz
Too hiigh
Too low
Frequency (Hz)
Check and fix electricity in one house
Unplug all devices and switch CB on
Check voltage at main connection
Check voltage at all sockets
Plug on the devices (one by one)
Check CB - if trip then the device is shorted
Check MCB - if trip then load is too high for one customer
Repeat from step 4 until broken devices known or max load identified
1) Before testing
2a) Good appliance
2b) Shorted appliance
GENERAL GUIDANCE
Wear appropriate safety gear and take precautions
  Never work with rotating parts before system is completely off
  Use gloves when dealing with cables and electricity even if the problem seems trivial and turn off switch
Use appropriate tools for the task at hand
If operators can’t fox or find the problem by themselves contact trained technician only
Overheated ELC or generator
Check water supply to ballast
Check under-greased/over-greased bearings
Check cooling water supply into ballast elements, replace if burnt/broken
Bad
Good
Bad
Good
Check if dust/anything blocked fan/ventilation
1). Properly greased
2a) under-greased
2b) over-greased
Good
Bad
Bad
Check fan ventilation blockage
*two actions are possible, try each one until solved
Concept and design by: Ari Bimo Prakoso and Robert Schultz, in collaboration with: Amalia Suryani and Thomas Strobel | ENDEV Indonesia © 2012
Is the turbine inlet (guide vane) fully open?
Notes: Shapes CHECK
Textboxes (Ya, Tidak) CHECK
3. Copyright Issue - I provide reference to trace them to free sources CHECK
Contact detail textboxes -- to supplemental poster
Clarification ( ….. CHECK
6. Content  simplify CHECK
7. Square, transparent (with/without frames) CHECK

## Slide 3
PLTMH: ___________________________
Operator: __________ HP: ___________
Manajer: __________ HP: ___________
Tersambung ke: ______ KK
Beda tinggi total: ____ m
Debit rata-rata: ____ l/s
Kapasitas terukur PLTMH: ____ kW
Tanggal komosioning: ____ /____ /____
Apakah generator/
Sabuk turbin berbunyi nyaring?
Matikan PLTMH
Atur kekencangan sabuk atau ganti sabuk yang telah rusak
Apakah saringan sampah bebas dan bersih dari hambatan?
Apakah frekuensi (Hz) pada panel kontrol PLTMH benar?
Kurang dari 48 Hz
Apakah dengan mengatur katup pada turbin untuk mengurangi aliran air dapat mengoreksi frekuensi (Hz) dan mengurangi bunyi?
Apakah lampu indikator ELC hijau?
Apakah ada mur pengencang yang longgar?
Kuatkan mur
Apakah ada peralatan/ pelanggan listrik yang baru?
Matikan peralatan yang baru
Tidak
Buka penuh inlet(katup pengatur) turbin
Apakah inlet (katup pengatur) turbin terbuka penuh?
Apakah lampu lebih terang?
Tidak
Periksa apakah ada MCB di rumah-rumah dan coba kurangi beban
(kapasitas generator terlampaui!)
Gunakan peralatan yang terpenting
Pasang saklar MCB di rumah-rumah
Apakah aliran air ke dalam turbin stabil, tidak terganggu, dan teratur?
Apakah ada sampah atau endapan di bak penenang atau saluran?
Apakah ada hambatan atau sampah di bendung?
Periksa penyumbatan pada pipa pesat dan katup pengatur turbin
Ya
Ya
Ya
Tidak
Tidak
Periksa tegangan (220 V) pada semua pelanggan yang tersambung pada cabang distribusi yang sama
Periksa apakah ada kabel yang putus dan sambungkan kembali
Periksa apakah ada terlalu banyak sambungan pelanggan
Tidak
Ya
50 Hz
Apakah saklar pemutus sirkuit ke pelanggan yang ada di rumah pembangkit NYALA?
Apakah generator dan turbin beroperasi dengan baik?
Nyalakan saklar pemutus sirkuit
Apakah saklar pemutus sirkuit mati lagi?
Tidak
Ya
1. Periksa apakah ada kabel yang korslet/arus pendek
dan
2. Periksa kelebihan beban pelanggan, dan coba kurangi beban (kapasitas generator terlampaui!)
Ya
Tidak
Bunyi Aneh?
Tidak Ada Listrik?
Terlalu Panas?
Apakah komponen ELC terbakar atau kotak ELC terlalu panas saat disentuh?
Apakah kipas ventilasi ELC bekerja dengan baik ?
Bersihkan kipas dan rumah kipas, ganti kipas jika perlu
Apakah sekering ballast pada ELC atau elemen ballast terbakar atau tidak tersambung?
1. Periksa apakah ada penyumbatan aliran air
dan
2. Periksa apakah ada kelebihan beban pelanggan, coba kurangi beban (kapasitas generator terlampaui!)
Apakah generator terlalu panas saat disentuh ?
Apakah kipas ventilasi pada rumah generator kotor atau terblokir?
Apakah arus beban (amp) pada amperemeter ELC di atas normal?
Ganti elemen yang terbakar, sambungkan kembali kabel dan/atau ganti sekering
Beri pelumas/gemuk dan periksa kerusakan pada bearing
Apakah ada bau terbakar dari dalam generator?
Matikan PLTMH, buka rumah generator, periksa apakah kumparan kabel kotor
Apakah ada bekas terbakar pada kumparan (arus pendek!)?
Bersihkan kumparan generator
Bersihkan kipas ventilasi dan rumah generator
Kurangi beban dengan mematikan peralatan dan/ atau pelanggan (kapasitas generator terlampaui!)
Apakah sabuk selip ketika PLTMH menyala?
Ganti bearing
Sesuaikan pelumas/gemuk ke kondisi normal
Atur kekencangan PLTMH
Ya
Ya
Tidak
Tidak
Ya
Tidak
Ya
Ya
Tidak
Ya
Tidak
Ya
Tidak
Bearing rusak
Terlalu sedikit/terlalu
banyak pelumas/gemuk
Normal
Ya
Apakah masalah terselesaikan setelah memeriksa dan memperbaiki listrik di rumah tersebut?
Ya
Ya
Ya
Ya
Periksa
Bangunan Sipil
Periksa Bangunan Sipil
?
Lampu Redup?
Semua pelanggan
Beberapa pelanggan
Satu pelanggan
Minta Bantuan
Nama teknisi: ___________________________________________
Nomor telepon teknisi: ____________________________________
Ya
Tidak
Minta Bantuan
Nama teknisi: ___________________________________________
Nomor telepon teknisi: ___________________________________
220 V
Periksa apakah ada kabel yang rusak dan sambungkan kembali
Lebih dari
52 Hz
Ya
Tidak*
Bersihkan saringan dari sampah
Tidak
Ya
Bersihkan bak penenang dan saluran
Tidak
Tidak*
Tidak*
Periksa apakah ada penyumbatan atau gangguan di sungai
Tidak*
Tidak
Tidak
Minta Bantuan
Nama teknisi: ___________________________________________
Nomor telepon teknisi: ___________________________________
Tidak*
1. Periksa penyumbatan aliran air
2. Periksa kebocoran air
Tidak*
*mungkin ada dua aksi, coba masing-masing sampai masalah terpecahkan
MCB sudah terpasang di rumah-rumah
Belum ada MCB di rumah-rumah
Untuk bunyi aneh, periksa frekuensi pada kotak panel
Lihat meter frekuensi pada kotak panel
Lihat apakah frekuensi
  Terlalu rendah: kurang dari 48 Hz
  Normal : 48 - 52 Hz
  Terlalu tinggi: lebih dari 52 Hz
Jika terlalu rendah, maka:
  Periksa apakah ada tambahan beban listrik/peralatan
  Periksa apakah ada pencurian listrik
  Periksa apakah aliran ke dalam turbin normal
Jika terlalu tinggi, atur aliran air ke turbin
Jika normal, periksa apakah aliran tidak stabil atau sabuk transmisi berbunyi nyaring
etr
48 Hz
52 Hz
Terlalu tinggi
Terlalu rendah
Frekuensi (Hz)
Memeriksa dan memperbaiki listrik di satu rumah
Lepas kabel semua alat dan nyalakan saklar CB
Periksa tegangan pada sambungan utama
Periksa tegangan pada semua colokan
Nyalakan alat-alat (satu demi satu)
Periksa CB - jika turun maka alat korslet
Periksa MCB - jika jatuh beban terlalu tinggi untuk satu pelanggan
Ulangi dari langkah 4, sampai peralatan yang rusak ditemukan atau beban maksimum diketahui
1) Sebelum tes
2a) Alat baik
2b) Alat korslet
PETUNJUK UMUM
Gunakan peralatan keamanan yang tepat dan berhati-hatilah:
  Jangan bekerja dengan mesin yang berputar sebelum sepenuhnya berhenti
  Gunakan sarung tangan ketika berurusan dengan kabel dan listrik walaupun masalah terlihat sepele dan saklar dalam keadaan mati
Gunakan alat yang tepat untuk pekerjaan
Jika operator tidak bisa memperbaiki atau menemukan masalah, hubungi teknisi terlatih
ELC atau generator terlalu panas
Periksa pasokan air ke ballast
Periksa apakah bearing terlalu banyak atau terlalu sedikit pelumas/gemuk
Periksa pasokan air pendingin ke elemen ballast, ganti jika rusak atau terbakar
Buruk
Baik
Buruk
Baik
Periksa jika debu/kotoran mengotori kipas/ventilasi
1). Dilumasi dengan baik
2a) Kurang pelumas
2b) Kebanyakan pelumas
Baik
Buruk
Buruk
Periksa penyumbatan pada kipas/ventilasi
*mungkin ada dua aksi, coba masing-masing sampai masalah terpecahkan
Konsep dan desain oleh: Ari Bimo Prakoso dan Robert Schultz, berkolaborasi dengan: Amalia Suryani dan Thomas Strobel | ENDEV Indonesia © 2012
Kurang dari 220 V
PANDUAN PEMECAHAN PERMASALAHAN MIKROHIDRO
Notes: Shapes CHECK
Textboxes (Ya, Tidak) CHECK
3. Copyright Issue - I provide reference to trace them to free sources CHECK
Contact detail textboxes -- to supplemental poster
Clarification ( ….. CHECK
6. Content  simplify CHECK
7. Square, transparent (with/without frames) CHECK